HYDRO-MAX

HM 1600

HYDRAULICALLY-DRIVEN

### AC GENERATOR

# BY

\

| QUALITY FEATURES |
| --- |
| Brushless AC Generator | Includes Pressure Compensating Flow Regulator |
| Maintenance Free Design | Lifetime Guaranteed Alignment |
| SPECIFICATIONS |
| Flow = | 19 GPM | Volts = | 120 or 120/240 |
| Pressure = | 2400 PSI | Amps = | 150 @ 120 |
| Speed = | 3600 RPM | Watts = | 16000 Continuous |
| Weight = | 135 Lbs | Power Factor = | 1.0 |
| Dimensions = | 9” W * 12.5” H * 29” L | Temperature Rating = | 105 C |

# Text boxes

120 /
240 V
60 Hz

16000
Watts
1 Phase

(845)-292-0800
http://www.getec.com

GETECK.COM

FERNDALE, NY 12734

Optional  Panel